## Slide 1
Telescope measurements
In nuclear physics, a “telescope”… is not a telescope!
It is an assembly of two or more detectors
that helps identifying particles mass and charge.
It is a powerful tool !!!

## Slide 2
Telescope measurements
It’s principle (here, a three stage telescope, Si, Si, CsI) :
E CsI
E Thick
E Thin
identification
Unknown incident particle

## Slide 3
Telescope measurements
Let see how it runs on a two stage telescope:
We simulate it with R:
R <- function (E, A, Z) 0.02442 * A / Z^2 * (E / A)^1.75
E <- function (R, A, Z) 8.3424 * A * (R * Z^2 / A)^0.57143
Th1 <- 0.3 #mm
Th2 <- 3 #mm
E1 <- function (E0, A, Z) {
ifelse (R(E0, A, Z) > Th1, E0 - E(R(E0, A, Z) - Th1, A, Z), E0)
}
E2 <- function (E0, A, Z) {
Er <- ifelse (R(E0, A, Z) > Th1, E(R(E0, A, Z) - Th1, A, Z), 0)
ifelse (R(Er, A, Z) > Th2, Er - E(R(Er, A, Z) - Th2, A, Z), Er)
}
* here, the material is… water
sorry

## Slide 4
Telescope measurements
Every time a unknown particle crosses one or the two detectors,
it shall be somewhere in the (Ethick, Ethin) plot:
12C
11C
10C
11B
10B
8B
10Be
9Be
7Be
7Li
6Li
4He
3He
t
d
p
Here 12C beam
On PMMA target
Possible identification
The particle crossed
both detectors…
The particle stopped
In the first detector

## Slide 5
Telescope measurements
During the experiment :
12C
11C
10C
11B
10B
8B
10Be
9Be
7Be
7Li
6Li
4He
3He
t
d
p
Here 12C beam
On PMMA target
Each point correspond to
a single particle

## Slide 6
Telescope measurements
Back home:
12C
11C
10C
11B
10B
8B
10Be
9Be
7Be
7Li
6Li
4He
3He
t
d
p
Here 12C beam
On PMMA target

## Slide 7
Telescope measurements
That’s all folks!
Telescopes are wonderful tools for charged particles identification
They shall be carefully designed with regard to
A, Z, E range of your specific experiment
For instance,
INDRA : IC, Si, CsI
Fragmentation : Si, Si, CsI
For new technics of identification, have a look at FAZIA!!!