## Slide 1
Neutron energy measurement
by Time Of Flight (TOF)
The problem :
In order to illustrate uncertainties measurement,
let’s have a look at neutrons energy measurement by TOF…
Particles beam
Active taget
Liquid scintillator
PM tube
neutron
L
start
stop
TOF
velocity
energy

## Slide 2
Neutron energy measurement
by Time Of Flight (TOF)
We suppose (for convenience) our neutron is not relativistic
It’s velocity is
And its energy
cm
ns
30cm/ns
m=940MeV/c²
L = 100cm
stop-start = 22.8 ns
 v = 0.146 c
 Ek = 10MeV
What is the uncertainty on Ek ?

## Slide 3
Neutron energy measurement
by Time Of Flight (TOF)
We know the liquid scintillator + PM + data acquisition system
We asked the colleagues that built the active target. They told us:
Anything else?
We assume the
distribution Gaussian

## Slide 4
Neutron energy measurement
by Time Of Flight (TOF)
What about the incident neutron interaction point ?
Th = 10cm
Interaction probability # 20% (we know it)
Interaction
Prob. Dens. Funct.
Reads “z follows an
Exponential pdf of
given rate”

## Slide 5
Neutron energy measurement
by Time Of Flight (TOF)
The interaction point follows about a uniform law
Th = 10cm

## Slide 6
Neutron energy measurement
by Time Of Flight (TOF)
The interaction point follows about a uniform law

## Slide 7
Neutron energy measurement
by Time Of Flight (TOF)
Uncertainty budget :
parameter
contribution
type
Interaction point uncertainty
start
stop
Uniform pdf
Normal pdf
Normal pdf
assumed
0.58 MeV
0.18 MeV
0.15 MeV
0.63 MeV
A
A
B
Combined uncertainty 

## Slide 8
Neutron energy measurement
by Time Of Flight (TOF)
Let’s compare what we did with
a full MC simulation :
MC results
Uncertainties
Budget result
Not so bad, in fact!
Moreover, now, we have the
equations of our problem at any energy and we
can play with them in order to OPTIMIZE our experiment!

## Slide 9
Neutron energy measurement
by Time Of Flight (TOF)
For instance: what are the result for a complete neutron spectrum
ranging from 5MeV to 40MeV ?
Beware :
Maybe we should
express energy with
relativistic corrections…
Beware :
Maybe we should
have included variable
detection efficiencies
But it’s not far from truth
Total
Interation point
Stop
start

## Slide 10
Neutron energy measurement
by Time Of Flight (TOF)
For instance: at what distance should we put the stop detector
in order to have it’s contribution to uncertainty lower than
other uncertainties (start & stop)?
We just have to express the uncertainty, making E apparent:
To see it’s not possible…
But we learn that

## Slide 11
Neutron energy measurement
by Time Of Flight (TOF)
Calculating uncertainties by the mean of metrology techniques
is not a mean to avoid MC approach's.
It is often harder (at the beginning) and it obliges you to focus
on important points
Thus, it gives you a deeper sight into your process
 It is a good way to OPTIMIZE your designs
MC techniques are generally the only way to get the pdf.
That’s all folks!